CCC System Trouble Codes

To pull codes, jumper pins A and B on the ALDL connector (upper right) and turn ignition switch to run position.

Code	Circuit or System		Probable Cause

12	No tach signal to ECM		This code will flash whenever the diagnostic terminal is grounded with the ignition turned On and the engine not

running.  If additional trouble codes are stored in the ECM they will appear after this code has flashed three times.  If

this	code appears while the engine is running, no reference pulses from the distributor are reaching the ECM.

13	Oxygen sensor Circuit		Check for a sticking or misadjusted throttle position sensor.  Check the wiring and connectors from the oxygen sensor.

Replace the oxygen sensor.

14	Coolant sensor/high temp	If the engine is experiencing overheating problems the problem must be rectified  before continuing.  Check all wiring

and connectors associated with the coolant temperature sensor.  Replace the coolant temperature sensor.

15	Cooland sensor/low temp	See above, then check the wiring connections at the ECM

21	Throttle position sensor/high	Check for a sticking or misadjusted TPS plunger.  Check all wiring and connections between the TPS and the ECM.

Adjust or replace the TPS.

22	Throttle position sensor/low	Check the TPS adjustment.  Check the ECM connector.  Replace the TPS.

23	Mixture control solenoid		The mixture control solenoid is open or grounded.

24	Vehicle speed sensor		A fault in this circuit should be indicated only when the vehicle is in motion.  Disregard Code 24 if it is set when the

drive wheels are not turning.  Check the connections at the ECM.  Check the TPS setting.

32	BARO circuit low		Barometric pressure sensor circuit low.

33	MAP Sensor			Check the vacuum hoses from the MAP sensor.  Check the electrical connections at the ECM.  Replace MAP sensor.

34	Vacuum sensor or MAP sensor	Code 34 will set when the signal voltage from the MAP sensor is too low.  Instead the ECM will substitute a fixed MAP

value and use the TPS to control fuel delivery.  Replace the MAP Sensor.

35	ISC valve			Idle Speed Contro error.  Replace the ISC.

41	EST circuit			No distributor reference pulses to the ECM at specified engine vacuum.

42	Electronic Spark Timing		Electronic Spark Timing bypass circuit or EST circuit is grounded or open.  A bad HEI module can cause this code.

43	Electronic spark control unit	The ESC retard signal has been on for too long or the system has failed a functional check.

44	Lean Exhaust			Check the ECM wiring connections, particularly terminals 15 and 8.  Check for vacuum leakage at the carb base

gasket, vacuum hoses or the intake manifold gasket.  Replace the oxygen sensor.

45	Rich Exhaust			Check the evaporative charcoal cansiter and it’s components for the presence of fuel.  Replace the oxygen sensor.

51	PROM or MEM-CAL		Make sure that the PROm or MEM-CAL is properly installed in the ECM.  Replace the PROM or MEM-CAL.

52	CALPAK			Check the CALPAK to insure proper installation.  Replace the CALPAK.

53	EGR Valve			Exhaust Gas Recirculation valve vacuum sensor has received improper EGR vacuum.

54	M/C solenoid			The mixture control solenoid voltage is high at the ECM because of a shorted M/C solenoid circuit and/or faulty ECM.

55	ECM				Be sure that the ECM ground connections are tight.  If they are, replace the ECM.

Component replacement may not cure the problem in all cases where recommended.  For this reason, you may want to seek professional advice before purchasing replacement parts.